## Slide 1: Update on the FTBF2018 Test beam and cosmic tests @ UVa
Kondo Gnanvo
EIC Weekly Meeting, Nov 26, 2018

## Slide 2: Test Beam Setup @ the FTBF June-July 2018
Large GEM @ Fermilab Test Beam Facility (FTBF) June-July 2018
Downstream GEM Trackers
Upstream GEM Trackers
Large EIC GEM prototype

## Slide 3: EIC-GT-GEM: Preliminary results on residuals from tracking
σy =144 µm
σx =372 µm
Offset correction performed x and y but however residual distribution mean is still around -0.5 mm for both x and y
  Need to correct for this discrepancy
The offset correction of z position of EIC-FT-GEM prototype as well as for the trackers not yet done
  Crude measurement of the z done manually but precise position need to be corrected by software
Multiple scattering effect negligible but no correction for tracking fit error
Expect resolution in y-direction to be below 100 µm, but here it is about 145 µm.
  Different potential causes: U-V strip readout layer quality? signal quality with zebra strip connection?
  gas flow rate in the chamber during the test beam? …Investigation ongoing

## Slide 4: µRWELL: Preliminary FTBF 2018 test beam results residuals from tracking
σy = 43 µm
σx =50 µm
Offset correction performed x and y but however residual distribution mean is still around -0.5 mm for both x and y
The offset correction of z position of EIC-FT-GEM prototype as well as for the trackers not yet done
  Crude measurement of the z done manually but precise position need to be corrected by software
Multiple scattering effect negligible but no correction for tracking fit error